## Slide 1
Vivian Nguyen, Dr. Kevin McFall
Southern Polytechnic College of Engineering and Engineering Technology
End to End Machine Learning Concept
The research is based on the NVIDIA DAVE-2 Self Driving Car: using a Convolutional Neural Network (CNN) to map raw pixels from a single front-facing camera directly to steering commands.
The goal of this system is to train a smaller robot to drive without explicit definition of any environment variables: lanes, edges, wall, obstacles, velocity, acceleration, direction.
Currently, this is being achieved by exploring the usage of PyTorch and Transfer Learning: using another well-trained CNN and training with collected data to drive autonomously.
Training Data is collected via camera input and associating velocity with motor encoder values from a quadrature motor with a 320x240 resolution image stored in a CSV file.
Verification of End to End Learning Concept for Mobile Robotics Platform
Robotics Platform
NVIDIA Jetson TX2 Development Board
NVIDIA JET Robotics Teaching Kit
Arduino Mega 2560
Webcam
DX5E/AR610 Transmitter/Receiver
Ongoing Results
Majority of the work done has been data collection and robot troubleshooting: differential drive calibration, RC transmitter ROS node communication.
Current Dataset: ~70,000 unique datapoints at ~1GB compressed images
The Autonomous Robot Platform
9 Datapoints with Associated Labeled Values
Current ROS Node Flowchart